## Slide 1: We Have Learned Last Time
Weekly Summary
Part II

## Slide 2: Announcement & Reminders (Oct 23)
Take-Home Quiz I:
  will try to get them graded by the end of this week!
  sample solutions will also be posted
Programming Project #2: due Friday Oct 29, 11:55pm
  please take a look at it – if have questions, send email to csci4211-help@cs.umn.edu
  Please start working on it, if you haven’t started yet
Written Homework Assignment #2 and Programming Project # 3 will be posted by Monday Oct 30!

## Slide 3: What We Have Learned Last Time (Oct 16)
  Review reliable data transfer protocols:
    stop-&-wait, & efficiency of protocols
    Go-back-N, selective repeat: window size & seq. no. space
  round trip time estimation and TCP timeoutInterval
TCP Flow Control: avoid overwhelm receiver
    RecvWin: receiver advertises available buffer space
Congestion Control: avoid overwhelm network routers
    two approaches: end-to-end implicit vs. router-assisted
  TCP congestion control: end-to-end implicit
    issue 1: how to determine network is congested
    issue 2: how to adjust sending rate to avoid congestion
    TCP congestion control mechanisms
      two parameters: ConWin, threshold
      slow start
      congestion avoidance: AIMD, duplicate ACKs, timeout
      fast retransmit/fast recovery

## Slide 4: TCP Flow Control: How It Works
(Suppose TCP receiver discards out-of-order segments)
spare room in buffer
= RcvWindow
= RcvBuffer-[LastByteRcvd - LastByteRead]
Rcvr advertises spare room by including value of RcvWindow in segments
Sender limits unACKed data to RcvWindow
  guarantees receive buffer doesn’t overflow

## Slide 5: TCP Slowstart
exponential increase (per RTT) in window size (not so slow!)
loss event: timeout (Tahoe TCP) and/or or three duplicate ACKs (Reno TCP)
initialize: Congwin = 1
for (each segment ACKed)
Congwin++
until (loss event OR
CongWin > threshold)
Slowstart algorithm
Host A
one segment
RTT
Host B
time
two segments
four segments
Notes: Here is an illustration of slow start. CongWin starts with 1 and after a round trip time it increases to 2, then 4 and so on. This exponential growth continues till there was any loss or the threshold is reached. After reaching threshold, we enter congestion avoidance phase which is described in the next slide. The loss may be detected either thru a timeout or duplicate acks.

## Slide 6: TCP Congestion Avoidance
/* slowstart is over */
/* Congwin > threshold */
Until (loss event) {
every W segments ACKed:
Congwin++
}
Threshold: = Congwin/2
Congwin = 1
perform slowstart
Congestion Avoidance
Notes: As mentioned before, a connection stays in slow start phase only till the threshold is reached. It then enters congestion avoidance phase where CongWin is increased by 1 for every round trip time. Essentially, CongWin is increased exponentially during slow start phase and linearly during congestion avoidance phase.
These phases are illustrated in the graph. Initially, CongWin is set to1. Between the round trip times 0 and 3, the connection is slow start phase and CongWin is increase to 8. At this point the threshold is reached and then on CongWin is increased by 1 for every RTT. This CongWin reaches the value of 12.
All this is when there were no losses. What happens when there is loss. Drastic action is taken. The threshold is set to current CongWin by 2. The CongWin is set to 1 and we are back in slow start phase. In the graph, where there was a loss when CongWin is 12. So the threshold is set 6, CongWin is set 1 and back to slow start phase.
This is how TCP adapts its congestion window based on packet successes/losses. This pattern of continually increasing and decreasing CongWin continues thru the lifetime of a connection and looks like a sawtooth pattern.

## Slide 7: TCP Congestion Control: Recap
end-end control (no network assistance)
sender limits transmission:
LastByteSent-LastByteAcked
CongWin
Roughly,
CongWin is dynamic, function of perceived network congestion
How does sender perceive congestion?
loss event = timeout or 3 duplicate ACKs
TCP sender reduces rate (CongWin) after loss event
three mechanisms:
  AIMD
  slow start
  conservative after timeout events
rate =
CongWin
RTT
Bytes/sec

## Slide 8: TCP Congestion Control: Recap (cont’d)
When CongWin is below threshold, sender in slow-start phase, window grows exponentially.
When CongWin is above Threshold, sender is in congestion-avoidance phase, window grows linearly.
When a triple duplicate ACKs occurs, threshold set to CongWin/2, and CongWin set to threshold.
When timeout occurs, threshold set to CongWin/2, and CongWin is set to 1 MSS.

## Slide 9: Announcement & Reminders (Oct 30)
Take-Home Quiz I:
  say something about the grading

## Slide 10: Announcement & Reminders (Oct 30)
Take-Home Quiz I graded, posted to Moodle?
Programming Project #2: due Sunday Oct 29, 11:55pm or extended?
Written Homework Assignment #2: posted today, due …
Programming Project # 3: posted by Monday Oct 30, due …
  Please take a look at the projct description, install the software, ....
  TA will be discussing it in next Monday’s class

## Slide 11: What We Learned Last Week (Oct 23)
Network Layer !
  basic functions: addressing, routing & forwarding
  IP addresses and IP prefixes:
    32 bits, dot notation
    two-level hierarchy: network part & host part
      how to determine network part?
    “classful” addressing scheme
    “classless” addressing scheme: CIDR
  Where do you get an IP address?
    manual config., or via DHCP -- how does it work?
  Where do you get an IP prefix?
  Network Service Model: IP Datagram service
    destination-based, hop-by-hop, forwarding
    forwarding (routing) table
    table look-up: longest prefix matching

## Slide 12: IP Addressing: Network vs. Host
Two-level hierarchy
  network part (high order bits)
  host part (low order bits)
What’s a network ?
(from IP address perspective)
  device interfaces with same network part of IP address
  can physically reach each other without intervening router
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
multi-access
LAN
point-to-point
link

## Slide 13: “Classful” IP Addressing
32 bits
0
network
host
10
network
host
110
network
host
1110
multicast address
A
B
C
D
class
1.0.0.0 to
127.255.255.255
128.0.0.0 to
191.255.255.255
192.0.0.0 to
223.255.255.255
224.0.0.0 to
239.255.255.255
7
7
15
23
31
  Disadvantage: inefficient use of address space, address space exhaustion
  e.g., class B net allocated enough addresses for 65K hosts, even if only 2K hosts in that network

## Slide 14: Classless Addressing: CIDR
CIDR: Classless InterDomain Routing
Network portion of address is of arbitrary length
Addresses allocated in contiguous blocks
  Number of addresses assigned always power of 2
Address format: a.b.c.d/x
  x is number of bits in network portion of address
11001000 00010111 00010000 00000000
network
part
host
part
200.23.16.0/23
Notes: Unlike in classfull addressing, under classless addressing, the length of the network portion of an address can be arbitrary. Consequently, it is not possible to figure out the network part from the address alone. We need to supply an additional information (network address mask) for that purpose. Now going back to the previous example, by allotting 11 bits for the host portion and 21 bits for the network portion, we can accommodate 2000 hosts without wasting much address space.

## Slide 15: Routing & Forwarding: Logical View of a Router
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
Notes: Here is an abstract view of the internals of a typical router. We can separate the functionality of a router into control plane and data plane. The control plane is responsible for exchanging routing information (control packets) with other routers and making routing decisions. Generally, there exists a route processor to process these control packets and to update the routing table. This routing table is then condensed into a form known as forwarding table for quick lookup by the data plane. The job of data plane is to switch packets from input ports to output ports, which is essentially a forwarding.engine. Data packets flow thru this faster data plane while control packets are processed by slower control plane. Another way to look at is that routing decisions are made by control plane and forwarding lookups done by data plane.

## Slide 16: Datagram Networks: the Internet model
no call setup at network layer
routers: no state about end-to-end connections
  no network-level concept of “connection”
packets forwarded using destination host address
  packets between same source-dest pair may take different paths, when intermediate routes change!
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Send data
2. Receive data

## Slide 17: Datagram vs. Virtual Circuit
Objective of both: move packets through routers from source to destination
Datagram Model:
  Routing: determine next hop to each destination a priori
  Forwarding: destination address in packet header, used at each hop to look up for next hop
    routes may change during “session”
  analogy: driving, asking directions at every gas station, or based on the road signs at every turn
Virtual Circuit Model (will be studied next week!):
  Routing: determine a path from source to each destination
  “Call” Set-up: fixed path (“virtual circuit”) set up at “call” setup time, remains fixed thru “call”
  Data Forwarding: each packet carries “tag” or “label” (virtual circuit id, VCI), which determines next hop
  routers maintain ”per-call” state

## Slide 18: IP Forwarding Table
4 billion possible entries!
(in reality, far less, but can still have millions of “routes”)
forwarding table entry format
destination network next-hop (IP address) link interface
(1st IP address , network mask )
11001000 00010111 00010000 00000000, 200.23.16.1 0
11111111 11111111 11111000 00000000
11001000 00010111 00011000 00000000, - (direct) 1
11111111 11111111 11111111 00000000
11001000 00010111 00011001 00000000, 200.23.25.6 2
11111111 11111111 11111000 00000000
otherwise 128.30.0.1 3

## Slide 19: Route aggregation: Shrinking the forwarding table
“Send me anything
with addresses
beginning
200.23.0.0/20”
200.23.2.0/23
200.23.4.0/23
200.23.14.0/23
UMN
Organization 0
CSE Department
Internet
Organization 1
200.23.6.0/23
Organization 2
.
.
.
.
.
.
Port 1
Port 0
Port 7
CSci4211: Network Layer: Part I

## Slide 20: Route aggregation with more specific routes
UMN-FAST has a more specific route to CSE department
“Send me anything
with addresses
beginning
200.23.0.0/20”
200.23.2.0/23
200.23.14.0/23
UMN
Organization 0
CSE Department
Internet
UMN-FAST
“Send me anything
with addresses
beginning
200.23.14.0/23”
200.23.4.0/23
Organization 2
.
.
.
.
.
.
CSci4211: Network Layer: Part I

## Slide 21: Forwarding Table & Longest Prefix Matching
21
Prefix Match Link Interface
11001000 00010111 00010 0
11001000 00010111 00011000 1
11001000 00010111 00011 2
otherwise 3
Equivalently:
CSci4211: Network Layer: Part I
Prefix Match Link Interface
200.23.16.0/21 0
200.23. 24.0/? 2
200.23.?.?/? 1
otherwise 3
Notes: 21

## Slide 22: Longest Prefix Matching
Prefix Match Link Interface
11001000 00010111 00010 0
11001000 00010111 00011 2
11001000 00010111 00011000 1
otherwise 3
DA: 11001000 00010111 00011000 10101010
Examples
DA: 11001000 00010111 00010110 10100001
interface 0
interface 1
But not interface 2, the 3rd entry
is also a match, but longer!
Interface 2?

## Slide 23: IP Forwarding: Destination in Same Net
Starting at A, send IP datagram addressed to B:
look up net. address of B in forwarding table
find B is on same net. as A
link layer will send datagram directly to B inside link-layer frame
  B and A are directly connected
misc
fields
223.1.1.1
223.1.1.3
data
Dest. Net. next router Nhops
223.1.1 1
223.1.2 223.1.1.4 2
223.1.3 223.1.1.4 2
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
forwarding table in A

## Slide 24: IP Forwarding: Destination in Diff. Net
Starting at A, dest. E:
look up network address of E in forwarding table
E on different network
  A, E not directly attached
routing table: next hop router to E is 223.1.1.4
link layer sends datagram to router 223.1.1.4 inside link-layer frame
datagram arrives at 223.1.1.4
continued…..
misc
fields
223.1.1.1
223.1.2.3
data
Dest. Net. next router Nhops
223.1.1 1
223.1.2 223.1.1.4 2
223.1.3 223.1.1.4 2
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
forwarding table in A

## Slide 25: IP Forwarding: Destination in Diff. Net …
Arriving at 223.1.4, destined for 223.1.2.2
look up network address of E in router’s forwarding table
E on same network as router’s interface 223.1.2.9
  router, E directly attached
link layer sends datagram to 223.1.2.2 inside link-layer frame via interface 223.1.2.9
datagram arrives at 223.1.2.2!!! (hooray!)
misc
fields
223.1.1.1
223.1.2.3
data
Dest. Net router Nhops interface
223.1.1 - 1 223.1.1.4
223.1.2 - 1 223.1.2.9
223.1.3 - 1 223.1.3.27
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
forwarding table in router

## Slide 26: What We Learned Last Time (Oct 23) cont’d
Data Link Layer
  Basic functions: framing, access control, etc.
MAC addresses and ARP (interactions of layers 2 &3)
  What is MAC address?
    How it differs from IP address
  Why do we need ARP
  How does ARP work?
Ethernet Frame Format
Bridges & Switches: connecting multiple LAN segments
  “plug-&-play”: cf. layer-1 repeater or layer-3 routers
  basic functions: forwarding/filtering frames
  switch forwarding table: self-learning alg.
    build switch table using the source MAC addr of a frame
    filter & forward based on dest. MAC addr: if there is an entry, forward using the output port; otherwise, “flood”

## Slide 27: Data Link Layer: Introduction
Some terminology:
hosts and routers are nodes
(bridges and switches too)
communication channels that connect adjacent nodes along communication path are links
  wired links
  wireless links
  LANs (local area networks)
layer 2 PDU (“packet”) referred to as frame, which encapsulates a layer-3 packet, e.g., an IP datagram
“link”

## Slide 28: Adaptors Communicating
sending side:
  encapsulates datagram in frame
  adds error checking bits, rdt, flow control, etc.
receiving side
  looks for errors, rdt, flow control, etc.
  extracts datagram, passes to upper layer at receiving side
controller
controller
sending host
receiving host
datagram
datagram
datagram
frame

## Slide 29: Ethernet Frame Structure
sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
preamble:
7 bytes with pattern 10101010 followed by one byte with pattern 10101011
used to synchronize receiver, sender clock rates
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 30: LAN Addresses and ARP
each adapter on LAN has unique LAN address
adapter
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)

## Slide 31: ARP Operation Illustration
Notes: Here is an illustration of ARP broadcast by W requesting hardware address of Y. As you can see, every node in the local physical network receive this request. Only Y sends the reply and also only to W.

## Slide 32
walkthrough: send datagram from A to B via R
  focus on addressing – at IP (datagram) and MAC layer (frame)
  assume A knows B’s IP address
  assume A knows IP address of first hop router, R (how?)
  assume A knows R’s MAC address (how?)
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
Forwarding to Another LAN

## Slide 33
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame with R's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
Forwarding to Another LAN

## Slide 34
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
frame sent from A to R
IP
Eth
Phy
frame received at R, datagram removed, passed up to IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222
Forwarding to Another LAN

## Slide 35
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy
Forwarding to Another LAN

## Slide 36
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as destination address, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy
Forwarding to Another LAN

## Slide 37
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
Forwarding to Another LAN

## Slide 38: Filtering/Forwarding
when frame received at switch:
  1. record incoming link, MAC address of sending host
  2. index switch table using MAC destination address
  3. if entry found for destination then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving
  interface */

## Slide 39: Questions?

## Slide 40
Switch/Bridge Self-Learning Algorithm
Spanning Tree Protocol
Router/Switch Architecture Overview
Generalization of IP Router and Ethernet Switch Data Plane Operations
  “match-action” forwarding abstraction
Openflow and Software-Defined Networking (SDN)
  Openflow switches
  Openflow protocol: control messages
  SDN controller (POX)
Software Switch (OVS) and Mininet
What We Learned Last Week (Oct 30)

## Slide 41: Self-learning, forwarding: example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
A A’
A A’
A A’
A A’
A A’
frame destination, A’, location unknown:
flood
A’ A
destination A location known:
selectively send
on just one link
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A’
4
60

## Slide 42: Interconnecting switches
self-learning switches can be connected together:
Q: sending from A to G - how does S1 know to forward frame destined to G via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 43: Spanning Tree Protocol
for increased reliability, desirable to have redundant, alternative paths from source to destination
with multiple paths, cycles result - switches may multiply and forward frame forever
solution: organize switches in a spanning tree by disabling subset of interfaces

## Slide 44: Router/Switch Architecture Overview
A key router/switch data plane function:
forwarding packets (e.g., IP datagrams, or Ethernet frames) from incoming to outgoing link (or drop them if no forwarding table entries, or flood them if no switching table entries
General CPU
NICs -- special hardware (ASICs)
varies depending on
“generations”
forwarding
operations
control
operations

## Slide 45: Input Port Functions
Decentralized switching:
using header field values, lookup output port using forwarding table in input port memory
goal: complete input port processing at ‘line speed’
queuing: if datagrams arrive faster than forwarding rate into switch fabric
Physical layer:
bit-level reception
Data link layer:
e.g., Ethernet
see chapter 6

## Slide 46: Input Port Queuing
Fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
output port contention:
only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric

## Slide 47: Output Ports
Buffering required when datagrams arrive from fabric faster than the transmission rate
Scheduling discipline chooses among queued datagrams for transmission
Datagram (packets) can be lost due to congestion, lack of buffers
Priority scheduling – who gets best performance, network neutrality

## Slide 48: Output Port Queueing
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric

## Slide 49
Switch/Bridge Self-Learning Algorithm
Spanning Tree Protocol
Router/Switch Architecture Overview
Generalization of IP Router and Ethernet Switch Data Plane Operations
  “match-action” forwarding abstraction
Openflow and Software-Defined Networking (SDN)
  Openflow switches
  Openflow protocol: control messages
  SDN controller (POX)
Software Switch (OVS) and Mininet
What We Learned Last Time (Oct 30) cont’d

## Slide 50
2
3
0100 1101
values in arriving
packet’s header
logically-centralized routing controller
1
control plane
data plane
Each switch contains a flow table that is computed and distributed by a logically centralized routing controller
local flow table
headers counters actions
Generalized Forwarding and SDN

## Slide 51: OpenFlow: Flow Table Entries
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Rule
Action
Stats
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Send to normal processing pipeline
Modify Fields
Packet + byte counters
Link layer
Network layer
Transport layer
Notes: Now I’ll describe the API that tries to meet these goals.
51

## Slide 52
Destination-based forwarding:
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
51.6.0.8
*
*
*
port6
IP datagrams destined to IP address 51.6.0.8 should be forwarded to router output port 6
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
*
*
*
*
22
drop
Firewall:
do not forward (block) all datagrams destined to TCP port 22
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
128.119.1.1
*
*
*
*
drop
do not forward (block) all datagrams sent by host 128.119.1.1
Examples

## Slide 53: OpenFlow Abstraction
IP Router
  match: longest destination IP prefix
  action: forward out a link
Layer-2 (Ethernet) Switch
  match: destination MAC address
  action: forward or flood
Firewall
  match: IP addresses and TCP/UDP port numbers
  action: permit or deny
NAT
  match: IP address and port
  action: rewrite address and port
match+action: unifies the data-plane operations of different kinds of routers, switches, and other devices

## Slide 54: OpenFlow example
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(3)
match
action
ingress port = 2
IP Dst = 10.2.0.3
ingress port = 2
IP Dst = 10.2.0.4
forward(3)
match
action
forward(4)
ingress port = 1
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(4)
match
action
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Example: datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2

## Slide 55: Simple SDN Network
Switch
Host1
Host2
Controller
L2 Forwarding
Controller APIs
Communication Protocol
Ethernet,IP,ARP,TCP,HTTP,…
POX, Floodlight, …
Software or Hardware

## Slide 56: Communication Protocol: OpenFlow (Main Components)
Flow tables
  Matching
  Manipulation
  Counters
Communication messages
  Controller to switch
  Asynchronous
  Symmetric
Controller
Pipeline
Secure Channel
Flow Table
Flow Table

## Slide 57: OpenFlow: Flow Tables (Structure)
A flow-table consists of
  a set of flow entries
  a table miss configuration
    Drop packet
    Send to controller
    Process using the next flow-table
Match fields | Counters | Instructions

## Slide 58: OpenFlow: Flow Tables (Processing)
Pipeline processing
Per table processing
  Find highest-priority matching ﬂow entry
  Apply instructions
    Modify packet & update match fields
    Update action set
    Update metadata
  Send match data and action set to next table

## Slide 59: OpenFlow: Communication Messages (Asynchronous)
Packet in All packets that do not have a matching flow entry are encapsulated and sent to the controller
Flow removed Sent to controller when flow expires due to idle or hard timeouts
Port status Generated if a port is brought down

## Slide 60: SDN Controller: POX
SDN controller written in Python
Many build-in modules
Python APIs to enable user extensions

## Slide 61: SDN Controller: POX (Built-in Modules)
Hub flood packets
L2 forwarding MAC learning
L3 forwarding IP learning
Topology discovery Underlying topology discovery
Spanning tree protocol Implementation of the standard STP
…

## Slide 62: SDN Controller: POX (Python APIs)
Event Management
openflow
L2 forwarding
Switch
Switch
POX Core
Handle
PacketIN
Packet
Raise PacketIn
Event
Firewall
Handle
PacketIN
(priority=100)
Packet
Packet
Register
Register

## Slide 63: SDN Controller: POX (Python APIs)

## Slide 64: Open vSwitch (Features)
Enables Linux to become part of the SDN architecture
Features
  L2-L4 matching
  VLANs with trunking
  Tunneling protocols such as GRE
  Remote configuration protocol
  Multi-table forwarding pipeline
  Monitoring via NetFlow, sFlow
  Spanning Tree Protocol
  Fine-grained QoS
  OpenFlow support
Runs in either
  Standalone mode
  OpenFlow mode

## Slide 65: Open vSwitch (Configuration)
Add a bridge and connect to controller
Host 1
VM1
br1
eth0
eth1
tap0
eth2
SDN
Controller

## Slide 66: Open vSwitch (Configuration)
Add a bridge and connect to controller

## Slide 67: Mininet (Architecture)
Mininet is a system for rapidly prototyping large networks on a single laptop

## Slide 68: Announcements & Reminders (Nov 13)
Homework Assignment #2 posted
  Due due Friday Nov 17 11:55pm
    5 big problems + 1 bonus problem
Project #3: due Sunday (Nov 19) 11:55pm
  if you have troubles w/ the project, ask TAs for help!
Take-Home Quiz 2:
Handout: Nov 20
Due: Nov 27 11:59pm

## Slide 69: What We Learned Last Time (Nov 06)
IP datagram format: TTL, datagram id, offset, flags, …
MTU & IP fragmentation & reassembly
NAT; brief overview of IPv6
Virtual Circuit and MPLS
  connection-oriented network service
    between hosts (or ingress/egress routers)
    need to connect set-up (“signaling”) before any data can be transmitted
  connection set-up (signaling) process:
    given a route/path, select (locally unique, outgoing) VCI, & set up VCI translation table at each router
  data forwarding:
    based on VCI carried in packets, perform VCI translation
VLAN: Virtual Local Area Network

## Slide 70: IP Datagram Format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
Internet
checksum
time to
live
32 bit source IP address
IP protocol version
number
header length
(bytes)
max number
remaining hops
(decremented at
each router)
for
fragmentation/
reassembly
total datagram
length (bytes)
upper layer protocol
to deliver payload to
head.
len
type of
service
“type” of data
flgs
fragment
offset
upper
layer
32 bit destination IP address
Options (if any)
E.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead with TCP?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead

## Slide 71: IP Fragmentation & Reassembly: Why
network links have MTU (max.transfer size) - largest possible link-level frame.
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly

## Slide 72: IP Fragmentation and Reassembly: Exp
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
One large datagram becomes
several smaller datagrams
Example
4000 byte datagram
MTU = 1500 bytes
offset in the second fragment:
185x8=1480
(why not 1500 bytes =length?)
offset in the third fragment:
370x8=2960
  Except for last fragment, IP fragment payload size (i.e., excluding IP header) must be multiple of 8!

## Slide 73: ICMP: Internet Control Message Protocol
used by hosts, routers, gateways to communication network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 dest port unreachable
3 4 datagram too big
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
5 0,1 redirect for network/host
8 0 echo request (ping)
9 0 route advertisement
10 0 router solicitation
11 0 TTL expired
12 0 bad IP header

## Slide 74
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0.0/24
rest of
Internet
datagrams with source or
destination in this network
have 10.0.0.0/24 address for
source, destination (as usual)
all datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,different source port numbers
NAT (Network Address Translation) A fix to limited IPv4 address space:

## Slide 75
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345
NAT (Network Address Translation)

## Slide 76: IPv6: Simplified Design
No checksum operation
No fragmentation
Longer addressing space
Fix size IP Header
2001:0db8:85a3:0000:0000:8a2e:0370:7334
Can have one or more
extension header fields
End hosts must perform path MTU
discovery (using ICMP) per destination
before sending any data!
data
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits

## Slide 77: Virtual Circuit: Signaling Protocols
used to setup, maintain teardown VC
used in ATM, frame-relay, X.25
used in part of today’s Internet: Multi-Protocol Label Switching (MPLS) operated at “layer 2+1/2” (between data link layer and network layer) for “traffic engineering” purpose
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Initiate call
2. incoming call
3. Accept call
4. Call connected
5. Data flow begins
6. Receive data

## Slide 78
During data packet forwarding phase, input VCI is used to look up the table, and is “swapped” w/ output VCI (VCI translation, or “label swapping”)
VCI translation table (aka “forwarding table”), built at call set-up phase
1
2
1
3
1
2
2
1
four “calls” going thru the router, each entry corresponding one call
green call
purple call
blue call
orange call
Notes: Here is an example of how VCI translation is done. Forwarding table maps a packet from an input port with input VCI to an output port and output VCI. This forwarding table is set up such that no two packets belonging to different connections (with different input VCIs or from different input ports) get switched to the same output port with same output VCI.
In this example, forwarding table says that a packet coming thru input port 1 with VCI 2 should be sent out on port 4 and VCI of the packet be changed to 1. Similarly packets from port 2 with VCI 1 are sent out on port 3 with VCI 2. You can see that no two output VCIs are same if the output port is also same.

## Slide 79: Virtual Circuit: Example
0
1
3
2
0
1
3
2
0
1
3
2
5
11
4
7
Router 3
Host B
Router 2
Host A
Router 1
Router 4
“call” from host A to host B along path:
host A router 1 router 2  router 3  host B
each router along path maintains an entry for the call in its VCI translation table
the entries piece together a “logical connection” for the call
Exercise: write down the VCI translation table entry for the call at each router

## Slide 80: Multiprotocol Label Switching (MPLS)
initial goal: speed up IP forwarding by using fixed length label (instead of IP address) to do forwarding
  borrowing ideas from Virtual Circuit (VC) approach
  but IP datagram still keeps IP address!
PPP or Ethernet
header
IP header
remainder of link-layer frame
MPLS header
label
Exp
S
TTL
20
3
1
8

## Slide 81: MPLS versus IP paths
R2
D
R3
R5
A
R6
IP router
IP routing: path to destination determined by destination address alone
R4

## Slide 82: MPLS versus IP paths
R2
D
R3
R4
R5
A
R6
IP-only
router
IP routing: path to destination determined by destination address alone
MPLS and
IP router
MPLS routing: path to destination can be based on source and destination address
  fast reroute: precompute backup routes in case of link failure
entry router (R4) can use different MPLS routes to A based, e.g., on source address

## Slide 83: VLANs: Motivation
consider:
CS user moves office to EE, but wants connect to CS switch?
single broadcast domain:
  all layer-2 broadcast traffic (ARP, DHCP, unknown location of destination MAC address) must cross entire LAN
  security/privacy, efficiency issues
Computer
Science
Electrical
Engineering
Computer
Engineering

## Slide 84: VLANs
port-based VLAN: switch ports grouped (by switch management software) so that single physical switch ……
switch(es) supporting VLAN capabilities can be configured to define multiple virtual LANS over single physical LAN infrastructure.
Virtual Local
Area Network
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
Electrical Engineering
(VLAN ports 1-8)
…
1
8
2
7
9
16
10
15
…
Computer Science
(VLAN ports 9-16)
… operates as multiple virtual switches

## Slide 85: A day in the life: scenario
Comcast network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
web page
browser

## Slide 86: A day in the life… connecting to the Internet
router
(runs DHCP)
connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP

## Slide 87: A day in the life… connecting to the Internet
router
(runs DHCP)
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply

## Slide 88: A day in the life… ARP (before DNS, before HTTP)
router
(runs DHCP)
before sending HTTP request, need IP address of www.google.com: DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
Eth
Phy
ARP
ARP
ARP reply

## Slide 89: A day in the life… using DNS
router
(runs DHCP)
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into Comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
demuxed to DNS server
DNS server replies to client with IP address of www.google.com
Comcast network
68.80.0.0/13
DNS server
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS

## Slide 90: A day in the life…TCP connection carrying HTTP
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
to send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in 3-way handshake) inter-domain routed to web server
TCP connection established!
64.233.169.105
web server
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
web server responds with TCP SYNACK (step 2 in 3-way handshake)

## Slide 91: A day in the life… HTTP request/reply
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
64.233.169.105
web server
HTTP
TCP
IP
Eth
Phy
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed

## Slide 92: Announcements & Reminders (Nov 20)
Project #3: due date extended to Wednesday (Nov 22) 11:55pm
  if you have troubles w/ the project, ask TAs for help!
Project #4: posted on class website, due Dec 10 11:55pm
Take-Home Quiz 2:
Handout: Nov 20
Due: Nov 27 11:59pm

## Slide 93: What We Learned Last Time (Nov 13)
Network Control Plane
  Conventional: per-router distributed control plane
  Emerging: centralized control plane via SDN controller
  Routing is a fundamental control plane operation
Two Basic (Distributed) Routing Algorithms:
  basic issues: exchange routing info & compute routes
  Link State vs. Distance Vector
    How does Link State (LS) work?
    How does Distance Vector (DV) work?
    Issue with DV: count-to-infinity & possible hacks

## Slide 94
Per-router Distributed Control Plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact with each other in control plane to compute forwarding tables
data
plane
control
plane

## Slide 95: Routing & Forwarding: Logical View of a (Classical) Router
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
Notes: Here is an abstract view of the internals of a typical router. We can separate the functionality of a router into control plane and data plane. The control plane is responsible for exchanging routing information (control packets) with other routers and making routing decisions. Generally, there exists a route processor to process these control packets and to update the routing table. This routing table is then condensed into a form known as forwarding table for quick lookup by the data plane. The job of data plane is to switch packets from input ports to output ports, which is essentially a forwarding.engine. Data packets flow thru this faster data plane while control packets are processed by slower control plane. Another way to look at is that routing decisions are made by control plane and forwarding lookups done by data plane.

## Slide 96
data
plane
control
plane
Logically Centralized Control Plane
A distinct (typically remote) controller interacts with local control agents (CAs) in routers to compute forwarding tables
Remote Controller
CA
CA
CA
CA
CA

## Slide 97: Routing: Issues
How are routing tables determined?
Who determines table entries?
What info used in determining table entries?
When do routing table entries change?
Where is routing info stored?
How to control routing table size?
Answer these questions, we are done!

## Slide 98: Routing Algorithms/Protocols
Routing algorithm/protocol goal: determine “good” paths (equivalently, routes), from sending hosts to receiving host, through network of routers
path: sequence of routers packets will traverse in going from given initial source host to given final destination host
“good”: least “cost”, “fastest”, “least congested”
routing: a “top-10” networking challenge!

## Slide 99: Graph Abstraction of the Network
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
aside: graph abstraction is useful in other network contexts, e.g.,
P2P, where N is set of peers and E is set of TCP connections

## Slide 100: Graph Abstraction: Costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x’) = cost of link (x,x’)
e.g., c(w,z) = 5
cost could always be 1, or
inversely related to bandwidth,
or inversely related to
congestion
cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
key question: what is the least-cost path between u and z ?
routing algorithm: algorithm that finds that least cost path

## Slide 101: Centralized vs. Distributed Routing Algorithms
Centralized:
A centralized route server collects routing information and network topology, makes route selection decisions, then distributes them to routers
Distributed:
Routers cooperate using a distributed protocol
  to create mutually consistent routing tables
Two standard distributed routing algorithms
  Link State (LS) routing
  Distance Vector (DV) routing

## Slide 102: Link State Algorithm
Basic idea: Distribute to all routers
  Topology of the network
    Cost of each link in the network
Each router independently computes optimal paths
  From itself to every destination
  Routes are guaranteed to be loop free if
    Each router sees the same cost for each link
    Uses the same algorithm to compute the best path
Notes: Under link state routing, each router gathers state of all the links in the network and then independently computes paths. Cost can be any generic metric capturing the link characteristics such bandwidth or delay.

## Slide 103: Link State vs. Distance Vector
Both assume that
  The address of each neighbor is known
  The cost of reaching each neighbor is known
Both find global information
  By exchanging routing info among neighbors
Differ in info exchanged and route computation
  LS: tells every other node its distance to neighbors
  DV: tells neighbors its distance to every other node

## Slide 104: Topology Dissemination
Each router creates a set of link state packets (LSPs)
  Describing its links to neighbors
  LSP contains
    Router id, neighbor’s id, and cost to its neighbor
Copies of LSPs are distributed to all routers
  Using controlled flooding
Each router maintains a topology database
  Database containing all LSPs
Notes: What is the cost of controlled flooding? A router would not forward an LSP more than once. Since each LSP carries a sequence number, a router can discard the duplicates by matching the originator and the sequence numbers with its LSP database.

## Slide 105: Topology Database: Example
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
link state database

## Slide 106: Constructing Routing Table: Dijkstra’s Algorithm
Given the network topology
  How to compute shortest path to each destination?
Some notation
  X: source node
  N: set of nodes to which shortest paths are known so far
    N is initially empty
  D(V): cost of known shortest path from source X
  C(U,V): cost of link U to V
    C(U,V) = if not neighbors

## Slide 107: Algorithm (at Node X)
Initialization
  N = {X}
  For all nodes V
    If V adjacent to X, D(V) = C(X,V) else D(V) =
Loop
  Find U not in N such that D(U) is smallest
  Add U into set N
  Update D(V) for all V not in N
    D(V) = min{D(V), D(U) + C(U,V)}
  Until all nodes in N

## Slide 108: Dijkstra’s Algorithm: Example
Step
0
1
2
3
4
5
start N
A
AD
ADE
ADEB
ADEBC
ADEBCF
D(B),p(B)
2,A
2,A
2,A
D(C),p(C)
5,A
4,D
3,E
3,E
D(D),p(D)
1,A
D(E),p(E)
infinity
2,D
D(F),p(F)
infinity
infinity
4,E
4,E
4,E
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
Notes: Suppose A wants to compute shortest paths to all other nodes. Initialization is like step 0. We add A itself to N and set the distance to all the neighbors as the cost of direct links and all others as infinity. Here D(B) is set 2 and D(E) set to infinity because B is a neighbor and E is not.
Now in step 1, among all those nodes that are not in N, we select a node with the shortest distance. In this case D is that node with distance of 1. First, we add D to the set N. Then we update the distances of other nodes if they can be made shorter by going thru D. In this case we can improve the distance to C from 5 to 4 by going thru D instead of using the direct link. Similarly E can now be reached with distance 2.
This way in each step, we pick the node with the shortest distance, add it to set N and update the distance of all other nodes not in N. After k iterations, shortest paths to nearest k neighbors are known. This process terminates after all the nodes are added to N.
This algorithm can be viewed as the construction of shortest paths spanning tree with source node as the root. In such a tree, there is exactly one path from the source node to any other node and that is the shortest path.

## Slide 109: Routing Table Computation
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
Notes: Now we know how to construct a shortest paths spanning tree. But what we want is the routing table. Question is how do we get the routing table from this tree? Routing table is essentially a mapping from destination to next hop. This can be obtained very easily from the shortest paths spanning tree. Consider each node and the path to that node. The first node along the path is the next hop.

## Slide 110: Distance Vector Routing
A router tells neighbors its distance to every router
  Communication between neighbors only
Based on Bellman-Ford algorithm
  Computes “shortest paths”
Each router maintains a distance table
  A row for each possible destination
  A column for each neighbor
    DX(Y,Z) : distance from X to Y via Z
Exchanges distance vector with neighbors
  Distance vector: current least cost to each destination
Notes: So far we have talked about link state routing. Under link state routing each router receives complete information about the network topology and computes shortest paths using Dijkstra’s algorithm. Now we will discuss a different routing protocol called distance vector Routing.
Under distance vector routing, a router informs its neighbors about the distance from that router to every other router in the network. Unlike in link state routing, here information is exchanged only between neighbors. It is based on Bellman-Ford algorithm for computing shortest paths. We will go through an example to see how this works.
Under distance vector routing, each router maintains a distance table. A row for each possible destination and a column for each neighbor. An entry in router X’s table corresponding to a row Y and a column Z is the distance from X to Y via Z.
Given a distance table we can find the shortest distance to a destination, i.e., the smallest value in the row corresponding to the destination. A list of <destination, shortest distance> tuples is called a distance vector and these distance vectors are exchanged between neighbors.

## Slide 111: Distance Table: Example
A
E
D
C
B
7
8
1
2
1
2
D ()
A
B
C
D
A
1
7
6
4
B
14
8
9
11
D
5
5
4
2
E
cost to destination via
destination
Notes: Lets look at an example. Here A, B, C, D, and E are routers and the links are labeled with their costs. And this is a distance table at router E. You can see that there is one row per each destination an one column per each neighbor.
If you look at the third row, it says that you can reach C via A with cost 6, via B with cost 9 and via D with 4. So the shortest distance to C is 4 via D. If E were to advertise its distance vector it will send <A,1>,<B,5>,<C,4>,<D,2>.

## Slide 112: Distance Vector Routing Algorithm
iterative:
continues until no nodes exchange info.
self-terminating: no “signal” to stop
asynchronous:
nodes need not exchange info/iterate in lock step!
distributed:
each node talks only with directly-attached neighbors
Distance Table data structure
each node has its own
row for each possible destination
column for each directly-attached neighbor to node
example: in node X, for dest. Y via neighbor Z:
D (Y,Z)
X
distance from X to
Y, via Z as next hop
c(X,Z) + min {D (Y,w)}
Z
w
=
=

## Slide 113: Distance Vector Routing: Overview
Iterative, asynchronous: each iteration caused by:
local link cost change
message from neighbor: its least cost path change from neighbor
Distributed:
each node notifies neighbors only when its least cost path to any destination changes
  neighbors then notify their neighbors if necessary
wait for (change in local link cost or msg from neighbor)
recompute distance table
if least cost path to any dest has changed, notify neighbors
Each node:

## Slide 114: Distance Vector Algorithm: Example
X
Z
1
2
7
Y
D (Y,Z)
X
c(X,Z) + min {D (Y,w)}
w
=
=
7+1 = 8
Z
D (Z,Y)
X
c(X,Y) + min {D (Z,w)}
w
=
=
2+1 = 3
Y

## Slide 115: Distance Vector Algorithm: Example
X
Z
1
2
7
Y

## Slide 116: Announcements & Reminders (Nov 27)
Take-Home Quiz 2: Due tonight 11:59pm
Project #4: posted on class website, due Dec 10 11:55pm
  TA will talk about it at the end of tonight’s lecture

## Slide 117: What We Learned Last Time (Nov 20)
Reviewed: Two Basic (Distributed) Routing Algorithms:
  basic issues: exchange routing info & compute routes
  Link State vs. Distance Vector
    How does Link State (LS) work?
    How does Distance Vector (DV) work?
    Issue with DV: count-to-infinity & possible hacks
Routing in Internet: two-level
Intra-domain routing (RIP, OSPF, IS-IS) – performance-based
vs. Inter domain routing: BGP – policy routing
Inter-domain Routing BGP
  ISP business models & AS relations
  BGP path vector routing, route filtering & selection processes, etc.

## Slide 118: Internet Structure
LANs
International lines
Regional or local ISP
local ISPs
company
university
National or tier-1 ISP
National or tier-1 ISP
IXPs
or private peering
Regional ISPs
company
access via WiFi hotspots
Internet: “networks of networks”!
Home users
Internet eXcange
Points
Home users

## Slide 119: Intra-AS and Inter-AS Routing
physical layer
“Gateways”:
  perform inter-AS routing amongst themselves
  perform intra-AS routers with other routers in their AS
inter-AS, intra-AS routing in
gateway A.c
network layer
link layer
a
b
b
a
a
C
A
B
d
A.a
A.c
C.b
B.a
c
b
c

## Slide 120: Intra-AS Routing
Also known as Interior Gateway Protocols (IGP)
Most common Intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First
  IS-IS: Intermediate System to Intermediate System (OSI Standard)
  EIGRP: Extended Interior Gateway Routing Protocol (Cisco proprietary)

## Slide 121: Path Attributes and BGP Routes
advertised prefix includes BGP attributes
  prefix + attributes = “route”
two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS
Policy-based routing:
  gateway receiving route advertisement uses import policy to accept/decline path (e.g., never route through AS Y).
  AS policy (export policy) also determines whether to advertise path to other other neighboring ASes

## Slide 122: eBGP, iBGP Connections
eBGP connectivity
iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
∂
∂
gateway routers run both eBGP and iBGP protocols

## Slide 123: BGP (Border Gateway Protocol)
The de facto standard (BGP-4)
Path Vector protocol:
  similar to Distance Vector protocol
  each Border Gateway broadcast to neighbors (peers) entire path (i.e., sequence of ASes) to destination
  BGP routes to networks (ASes), not individual hosts
E.g., Gateway X may announce to its neighbors it “knows” a (AS) path to a destination network, Z, via a series of ASes:
Path (X,Z) = X,Y1,Y2,Y3,…,Z
BGP border gateways referred to as BGP speakers

## Slide 124: BGP Operations: Policy Routing
Q: What does a BGP border gateway do?
Receiving and filtering route advertisements from directly attached neighbor(s)
  To accept or not accept route advertisements depends on policies (e.g., whether you “trust” your neighbors)
Route selection (rank diff. routes to same dest. network).
  to route to destination X, which path (of several advertised) will be taken?
  route selection based on policies (e.g., always prefer route advertisement from “good old” neighbor Y)
Filtering and sending (certain) route advertisements to neighbors
  what/whether to advertise to your neighbors also depends on policies (e.g., don’t tell your neighbor Z that you know a route to destination X)

## Slide 125: BGP Path Advertisement
AS1 gateway router 1c learns path AS2,AS3,X from 2a
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
gateway router may learn about multiple paths to destination:
AS3,X
AS1 gateway router 1c learns path AS3,X from 3a
Based on policy, AS1 gateway router 1c chooses path AS3,X, and advertises path within AS1 via iBGP

## Slide 126: BGP Example
Speaker for AS2 advertises reachability to P and Q
  network 128.96/16, 192.4.153/24, 192.4.32/24, and 192.4.3/24, can be reached directly from AS2
Speaker for backbone advertises
  networks 128.96/16, 192.4.153/24, 192.4.32/24, and 192.4.3/24 can be reached along the path (AS1, AS2).
Speaker can cancel previously advertised paths (by sending withdrawal messages)
Backbone network
(AS 1)
Regional provider A
(AS 2)
Regional provider B
(AS 3)
Customer P
(AS 4)
Customer Q
(AS 5)
Customer R
(AS 6)
Customer S
(AS 7)
128.96/16
192.4.153/24
192.4.32/24
192.4.3/24
192.12.69/24
192.4.54/24
192.4.23/24

## Slide 127: BGP Attributes
Value Code Reference
----- --------------------------------- ---------
1 ORIGIN [RFC1771]
2 AS_PATH [RFC1771]
3 NEXT_HOP [RFC1771]
4 MULTI_EXIT_DISC [RFC1771]
5 LOCAL_PREF [RFC1771]
6 ATOMIC_AGGREGATE [RFC1771]
7 AGGREGATOR [RFC1771]
8 COMMUNITY [RFC1997]
9 ORIGINATOR_ID [RFC2796]
10 CLUSTER_LIST [RFC2796]
11 DPA [Chen]
12 ADVERTISER [RFC1863]
13 RCID_PATH / CLUSTER_ID [RFC1863]
14 MP_REACH_NLRI [RFC2283]
15 MP_UNREACH_NLRI [RFC2283]
16 EXTENDED COMMUNITIES [Rosen]
...
255 reserved for development
From IANA: http://www.iana.org/assignments/bgp-parameters
Most
important
attributes
Not all attributes
need to be present in
every announcement

## Slide 128: Customers and Providers
Customer pays provider for access to the Internet
provider
customer
IP traffic
provider
customer

## Slide 129: The Peering Relationship
peer
peer
customer
provider
Peers provide transit between
their respective customers
Peers do not provide transit
between peers
Peers (often) do not exchange $$$
traffic
allowed
traffic NOT
allowed

## Slide 130: Peering Provides Shortcuts
Peering also allows connectivity between
the customers of “Tier 1” providers.
peer
peer
customer
provider

## Slide 131: Announcements & Reminders (Dec 4)
Take-Home Quiz 2: still being graded
Project #4: due on Sunday Dec 10 11:55pm
Final Exam: Mon Dec 18 6:30pm – 8:30pm,
in-class
open book, open nots, & open “Internet”
(but no communications w/ fellow students or anyone else!)
  If you have final conflicts, or special needs, please let us know ASAP
Next Monday: wrap-up & reviews
  Will send you a sample final exam for you to practice this week/weekend

## Slide 132: Take Home Quiz 2 & Other Tidbits
Take-Home Quiz II: graded (rather leniently)!
  statistics: Max. 123, Median 105, Mean 100, Min. 38
Not counting students who did not turn or cheated on the quiz.
Please feel free to talk to us if you have questions, especially if you didn’t do well
Points # people
[110-125] 22
[100-109] 22
[90-99] 12
[80-89] 3
[70-79] 3
[60-69] 4
[0-59] 1
Total 67

## Slide 133: What We Learned Last Time (Nov 27)
Routing in Internet: two-level
Intra-domain routing (RIP, OSPF, IS-IS) – performance-based
vs. Inter domain routing: BGP – policy routing
Inter-domain Routing BGP
  ISP business models & AS relations
  BGP path vector routing, route filtering & best route selection processes, etc.
    filter routers to a neighbor AS (customer, peer or provider): customer routes ? peer routes? provider routes?
    Which route to select: customer routes, peer routes vs. provider routes?
Data Link Layer Revisited:
  Framing & checksum/CRC
  point-to-point link: PPP -- byte stuffing
  media access control: taxonomy: take turns vs. random access

## Slide 134: BGP Example
U, X are providers of A; V & X are providers of B; U & W is a provider of C
U, V are providers of X;
U, V, & W are peers
How are routes from AS A, B & C propagated to the rest of the ASes?
How many routes regarding 128.101.54.0/24 are received by A? Which route does it choose as its “best route” to it?
192.4.153.0/24
128.101.54.0/24
134.14.10.0/20
78.34.0.0/16

## Slide 135: Adaptors Communicating
sending side:
  encapsulates datagram in frame
  adds error checking bits, rdt, flow control, etc.
receiving side
  looks for errors, rdt, flow control, etc.
  extracts datagram, passes to upper layer at receiving side
controller
controller
sending host
receiving host
datagram
datagram
datagram
frame

## Slide 136: Error Detection
EDC= Error Detection and Correction bits (redundancy)
D = Data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction

## Slide 137: PPP Data Frame
info: upper layer data being carried
check: cyclic redundancy check for error detection

## Slide 138: Byte Stuffing
flag byte
pattern
in data
to send
flag byte pattern plus
stuffed byte in transmitted data
0 1 1 1 1 1 1 0
0 1 1 1 1 1 1 0

## Slide 139: Multiple Access Links: MAC Protocols
two types of “links”:
point-to-point
  PPP for dial-up access
  point-to-point link between Ethernet switch, host (PPPoE)
broadcast (shared wire or medium)
  old-fashioned Ethernet
  upstream HFC
  802.11 wireless LAN
shared wire (e.g.,
cabled Ethernet)
shared RF
(e.g., 802.11 WiFi)
shared RF
(satellite)
humans at a
cocktail party
(shared air, acoustical)

## Slide 140: Taxonomy of MAC Protocols
polling
CSMA/CA
(WiFi/802.11)

## Slide 141: Announcements & Reminders (Dec 11)
Final Exam: Mon Dec 18 6:30pm – 8:30pm,
in-class
open book, open nots, & open “Internet”
(but no communications w/ fellow students or anyone else!)
  If you have final conflicts, or special needs, please let us know ASAP
Extra office hours:
  This Friday: 4pm – 6pm
  Next Monday: 4pm - 6pm (& by appointment earlier of the day)
  TAs will hold extra office hours this week!
Questions & concerns with homework/project grading, please contact TAs and/o me ASAP.

## Slide 142: What We Learned Last Time (Dec 11)
  Media Access Control: Shared media
    issues and difficulties
Taxonomy of MAC Protocols
  Random Access Control:
    ALOHA and Slotted ALOHA
    CSMA: nonpersistent vs. p-persistent
    CSMA/CD
    What are they? How do they work?
  Adaptive Controlled Access:
    token passing vs. polling
  Efficiency of MAC protocols: light vs. heavy load
Ethernet (802.3)
  MAC: 1-persistent CSMA/CD, binary random backoff
  collision domain, bit-time and min. frame size
  10BaseT, 100 BaseT (Fast Ethernet), Gigabit Ethernet

## Slide 143: What We Learned Last Time (Dec 11) …
  802.11b and Wireless LAN:
  key issues & difficulties:
    hidden terminal problem, power saving requirement
  receiver acknowledgement needed!
    how does it work? SIFS < DIFS
  CSMA/CA: how does it work? RTS, CTS, NAV
  802.11 frame format & frame forwarding via APs
    Why 3 (or 4) addresses? How are they used?
Today: briefly
  Bluetooth
  Token Ring (802.5)
    token passing
    ring maintenance issues
  Optional: (LAN & wide-area) mobility; cellular networks
  Wrap-up & Review

## Slide 144: Ethernet and IEEE 802.3
1-persistent CSMA/CD
Carrier sense: station listens to channel first
  Listen before talking
If idle, station may initiate transmission
  Talk if quiet
Collision detection: continuously monitor channel
  Listen while talking
If collision, stop transmission
  One talker at a time
Notes: CSMA/CD protocol is standardized and referred to as IEEE 802.3. Ethernet employs 1-persistent CSMA/CD. It senses the channel and transmits if idle. Otherwise it will wait till it becomes idle and attempts transmission. In case of a collision, it backs off for a random time.

## Slide 145: Ethernet CSMA/CD Algorithm
1. Adaptor gets datagram from and creates frame
2. If adapter senses channel idle, it starts to transmit frame. If it senses channel busy, waits until channel idle and then transmits
3. If adapter transmits entire frame without detecting another transmission, the adapter is done with frame ! Signal to network layer “transmit OK”
4. If adapter detects another transmission while transmitting, aborts and sends jam signal
5. After aborting, adapter enters exponential backoff: after the mth collision, adapter chooses a K at random from {0,1,2,…,2m-1}. Adapter waits K*512 bit times and returns to Step 2
6. Quit after 16 attempts, signal to network layer “transmit error”

## Slide 146: Worst Case Collision Detection Time
Notes: Here is an illustration of the worst case. If the two stations are farthest apart, it takes up to twice the signal propagation time to realize that collision occurred. So a station would know whether it has seized the channel or not only after round trip propagation delay.

## Slide 147: Ethernet’s CSMA/CD (more)
Jam Signal: make sure all other transmitters are aware of collision; 48 bits;
Bit time: .1 microsec for 10 Mbps Ethernet ; for K=1023, wait time is about 50 msec
Exponential Backoff:
Goal: adapt retransmission attempts to estimated current load
  heavy load: random wait will be longer
first collision: choose K from {0,1}; delay is K x 512 bit transmission times
after second collision: choose K from {0,1,2,3}…
after ten collisions, choose K from {0,1,2,3,4,…,1023}
See/interact with Java
applet on AWL Web site:
highly recommended !

## Slide 148: IEEE 802.3 Parameters
1 bit time = time to transmit one bit
  10 Mbps  1 bit time = 0.1 microseconds
Maximum network diameter <= 2.5km
  Maximum 4 repeaters
“Collision Domain”
  Distance within which collision can be detected
  IEEE 802.3 specifies:
worst case collision detection time: 51.2
Why minimum frame size?
  51.2 => minimum # of bits can be transited at 10Mpbs is 512 bits => 64 bytes is required for collision detection
Notes: Ethernet specification limits the cable length to be no more than 2.5 Km with at most 4 repeaters. This corresponds to a round trip propagation delay of approximately 51.2 microseconds. As pointed out earlier this gives the worst case time to detect a collision. So only after 51.2 microseconds a station would know for sure that it has seized the channel and there would not be a collision during its transmission.
This also puts a constraint on the minimum frame size. In case of 10Mbps Ethernet, transmission of 64 bytes takes 51.2 micro seconds. If the packet size is less than 64 bytes, packet transmission time would be less than the worst case collision detection time. Transmission would be complete before the station can be sure that it has seized the channel. This is not desirable and so the frame size should be at least 64 bytes.
This implies that data in Ethernet frame should be at least 46 bytes considering that SA, DA, LEN, CRC together take up 18 bytes. If the data is smaller than 46 bytes, it is padded to fill out the frame to minimum size.

## Slide 149: 100Base T (Fast) Ethernet: Issues
1 bit time = time to transmit one bit
  100 Mbps  1 bit time = 0.01 (microseconds)
If we keep the same “collision domain”, i.e.,
worst case collision detection time kept at 51.2 (microseconds
  Q: What will be the minimum frame size?
  51.2 => minimum # of bits can be transited at 100Mpbs is 5120 bits => 640 bytes is required for collision detection
  This requires change of frame format and protocol!
Or we can keep the same minimum frame size, but reduce “collision domain” or network diameter!
  from 51.2 to 5.12 !
  maximum network diameter 100 m!

## Slide 150: Gigabit Ethernet & Beyond
Gigabit Ethernet:
use standard Ethernet frame format
allows for point-to-point links and shared broadcast channels
in shared mode, CSMA/CD is used; short distances between nodes to be efficient
  also uses hubs, called “Buffered Distributors”
Full-Duplex at 1 Gbps for point-to-point links
Now: 10 & 40 Gbps are widely available
And 100 Gbps is also here !
All are used in “point-to-point” settings with Ethernet switches

## Slide 151: 802.11 LAN Infrastructure Mode
wireless host communicates with base station
  base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
hub, switch
or router
AP
AP

## Slide 152: 802.11: Channels, Association
802.11b: 2.4GHz-2.485GHz spectrum divided into 11 channels at different frequencies
  AP admin chooses frequency for AP
  interference possible: channel can be same as that chosen by neighboring AP!
host: must associate with an AP
  scans channels, listening for beacon frames containing AP’s name (SSID) and MAC address
  selects AP to associate with
  may perform authentication [Chapter 8]
  will typically run DHCP to get IP address in AP’s subnet

## Slide 153: 802.11: Passive/Active scanning
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
3
1
passive scanning:
beacon frames sent from APs
association Request frame sent: H1 to selected AP
association Response frame sent from selected AP to H1
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
2
3
4
active scanning:
Probe Request frame broadcast from H1
Probe Response frames sent from APs
Association Request frame sent: H1 to selected AP
Association Response frame sent from selected AP to H1

## Slide 154: Ad Hoc Network Approach
No access point (i.e., base station)
  “peer-to-peer” mode
wireless hosts communicate with each other
  to get packet from wireless host A to B may need to route through wireless hosts X,Y,Z
Applications:
  “laptop” meeting in conference room, car
  interconnection of “personal” devices
  battlefield
IETF MANET (Mobile Ad hoc Networks) working group

## Slide 155: Wireless Network Characteristics (again!)
Multiple wireless senders and receivers create additional problems (beyond multiple access):
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other
means A, C unaware of their interference at B
A
B
C
A’s signal
strength
space
C’s signal
strength
Signal fading:
B, A hear each other
B, C hear each other
A, C can not hear each other interferring at B

## Slide 156: Hidden and Exposed Terminal Problems
Wireless networks: hidden and exposed nodes
  A->B and C->B: A can’t hear C’s transmission
    C hidden from A, can cause collision!
  B->A and C->D: won’t interfere with each other, despite B can hear C’s transmission
    C exposed to B,
    unnecessary backoff by B!

## Slide 157: IEEE 802.11: Multiple Access
avoid collisions: 2+ nodes transmitting at same time
802.11: CSMA - sense before transmitting
  don’t collide with ongoing transmission by other node
802.11: no collision detection!
  difficult to receive (sense collisions) when transmitting due to weak received signals (fading);
    often need to switch between transmitting vs. receiving mode
  can’t sense all collisions in any case: hidden terminal, fading
  goal: avoid collisions: CSMA/C(ollision)A(voidance)
A
B
C
A
B
C
A’s signal
strength
space
C’s signal
strength

## Slide 158: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 sender
1 if sense channel idle for DIFS then
  transmit entire frame (no CD)
2 if sense channel busy then
  start random backoff timer
  timer counts down while channel idle
  transmit when timer expires
if no ACK (e.g., due to collision or bit error), increase random backoff interval, repeat 2
802.11 receiver
- if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
sender
receiver
DIFS
data
SIFS
ACK

## Slide 159: Collision Avoidance Mechanisms
Problem:
  two nodes, hidden from each other, transmit complete frames to base station
  wasted bandwidth for long duration !
Solution:
  small reservation packets
  nodes track reservation interval with internal “network allocation vector” (NAV)

## Slide 160: Avoiding Collisions (cont’d)
idea: allow sender to “reserve” channel rather than random access of data frames: avoid collisions of long data frames
sender first transmits small request-to-send (RTS) packets to BS using CSMA
  RTSs may still collide with each other (but they’re short)
BS broadcasts clear-to-send CTS in response to RTS
RTS heard by all nodes
  sender transmits data frame
  other stations defer transmissions
Avoid (large) data frame collisions
using small reservation packets!

## Slide 161: Collision Avoidance: Some Details
Sender transmits RequestToSend (RTS) frame
Receiver replies with ClearToSend (CTS) frame
Neighbors…
  see CTS: keep quiet
  see RTS but not CTS: ok to transmit
Receiver sends ACK when has frame
  neighbors silent until see ACK
Collisions
  no collisions detection
  known when don’t receive CTS
  exponential backoff

## Slide 162: Collision Avoidance: RTS-CTS Exchange
sender transmits short RTS (request to send) packet: indicates duration of transmission
receiver replies with short CTS (clear to send) packet
  notifying (possibly hidden) nodes
hidden nodes will not transmit for specified duration: NAV

## Slide 163: Collision Avoidance: RTS-CTS Exchange
AP
A
B
time
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer

## Slide 164: 802.11 Frame: Addressing
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Address 2: MAC address
of wireless host or AP
transmitting this frame
Address 1: MAC address
of wireless host or AP
to receive this frame
Address 3: MAC address of original (i.e., actual!) source or target (i.e., actual) destination when frames are forwarded by AP
Address 4: used when frames are forwarded from one AP to another AP (MAC address of actual source)

## Slide 165
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Type
From
AP
Subtype
To
AP
More
frag
WEP
More
data
Power
mgt
Retry
Rsvd
Protocol
version
2
2
4
1
1
1
1
1
1
1
1
802.11 Frame: More
duration of reserved
transmission time (RTS/CTS)
frame seq #
(for reliable ARQ)
frame type
(RTS, CTS, ACK, data)

## Slide 166
Internet
router
AP
H1
R1
AP MAC addr H1 MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
R1 MAC addr H1 MAC addr
dest. address
source address
802.3 frame
802.11 Frame: Addressing
To-AP=1; From-AP=0;
Not AP’s MAC address!

## Slide 167
Internet
router
AP
H1
R1
H1 MAC addr AP MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
H1 MAC addr R1 MAC addr
dest. address
source address
802.3 frame
802.11 Frame: Addressing
To-AP=0; From-AP=1;

## Slide 168: Questions?